## Slide 1: CHBE 552 Project Comparison of the Gauss-Newton Method with the Simplex Optimization Method for Parameter Estimation in Algebraic Models
Jincong Li
April 7th

## Slide 2: Outline
Gauss-Newton Method with Marquardt’s Modification
Nelder-Mead Algorithm
Problem 1: Adsorption of 1,2 Dichloropropane
Problem 2: MnO2-Catalyzed Acetic Acid Oxidation

## Slide 3: Gauss-Newton Method with Marquardt’s Modification
Gauss-Newton Method for Non-Linear Least Squares:
    Aim: Minimize sum of squared differences between observed data and model predictions.
    Application: Parameter estimation in models linearizable with respect to parameters.
    Iterative Approach: Refines parameter estimates to reduce discrepancy between observed and predicted values.
    Update Formula: where J is the Jacobian matrix and r is the residuals vector.

## Slide 4: Gauss-Newton Method with Marquardt’s Modification
Marquardt’s Modification (Levenberg-Marquardt Algorithm):
    Enhancement of Gauss-Newton method, introducing a damping factor λ for robustness.
    Improves convergence, especially when the Jacobian is near singular or not invertible.
    Combined Approach: Acts like gradient descent with high λ and like Gauss-Newton with low λ.
    Modified Update Formula: adding flexibility to step size and direction.
    Goal: Achieve balance between speed (Gauss-Newton) and stability (gradient descent) in parameter estimation.

## Slide 5: Gauss-Newton Method with Marquardt’s Modification
Computing Confidence Intervals for Parameter Estimates:
    Covariance Matrix Calculation:
      Derived from the inverse of the Hessian matrix, approximated by J^T*J, where J is the Jacobian matrix.
      Use the pseudo-inverse in cases of singularity for stability.
    Standard Errors of Estimates:
      Calculated as the square root of the diagonal elements of the covariance matrix.
    Confidence Interval Calculation:
      Confidence intervals are determined using the standard errors, a critical value from the t-distribution, and the degrees of freedom.
      Formula: Estimate±(t-critical×Standard Error)

## Slide 6: Nelder-Mead Algorithm
Direct search method for minimizing an objective function.
Suitable for non-linear, non-smooth functions without requiring derivatives.
Operates using a simplex (a polytope in higher dimensions) to represent candidate solutions.

## Slide 7: Nelder-Mead Algorithm
Key Steps of the Nelder-Mead Method:
    Initialization: Generate an initial simplex around a starting point.
    Evaluation: Calculate the objective function at each simplex vertex.
    Transformation: Perform operations to update the simplex:
    Reflection: Reflect the worst point across the centroid if it improves.
    Expansion: Take a larger step if reflection finds a new best point.
    Contraction: Move the worst point closer to the centroid if reflection fails.
    Shrinkage: Reduce the simplex size around the best point for finer exploration.
    Termination: Repeat until reaching a stop condition (e.g., minimal objective function change, small simplex, maximum iterations).

## Slide 8: Nelder-Mead Algorithm
Advantages: Simple implementation, no need for derivative information, versatile across complex functions.
Limitations: Potential for slow convergence or convergence to non-optimal points, especially in rugged landscapes or high dimensions.
Applications: Ideal for parameter estimation in models where gradient-based methods are inapplicable due to lack of derivatives or presence of many local minima.

## Slide 9: Nelder-Mead Algorithm
Bootstrap Method Overview:
    A statistical tool to estimate the distribution of a statistic (e.g., mean, variance) from data.
    Involves sampling with replacement to create many "bootstrap samples."
    Computes the statistic for each bootstrap sample to generate a distribution.
Key Steps:
    Resampling: Randomly sample with replacement from the original data to create bootstrap samples.
    Computation: Calculate the statistic of interest for each bootstrap sample.
    Repetition: Repeat the resampling and computation steps many times to build a distribution.
    Estimation: Use the distribution to estimate confidence intervals or variance of the statistic.

## Slide 10: Nelder-Mead Algorithm
Number of Iterations: More iterations increase the accuracy of the confidence interval estimates but also require more computational resources.
Random Sampling with Replacement: Ensures that each bootstrap sample is an independent and identically distributed sample of the data, mirroring the sampling variability in the original dataset.
Applicability: While bootstrap is widely applicable, its validity depends on the data being representative of the population. In cases where the original sample may not represent the population well, bootstrap estimates may be biased.

## Slide 11: Problem 1: Adsorption of 1,2 Dichloropropane
Determine the parameters () of the adsorption model (equation 1) of [1]
    : amount adsorbed
    : saturation amount adsorbed
    : equilibrium constant
    : pressure
    : parameter that characterizes the system heterogeneity
Determine the 95 % confidence interval of the parameters

## Slide 12: Problem 1: Adsorption of 1,2 Dichloropropane
Figure 1: Raw Data for Problem [1]

## Slide 13: Problem 1: Adsorption of 1,2 Dichloropropane
Result
    By GN-M:
Validation
T | q_sat | k | t
303 | 4.31 ± 0.19 | 17.73 ± 5.73 | 0.46 ± 0.05
338 | 5.2 ± 0.56 | 7.99 ± 2.6 | 0.37 ± 0.05
373 | 4.56 ± 1.09 | 1.72 ± 0.41 | 0.38 ± 0.07
423 | 6.77 ± 6.75 | 0.8 ± 0.23 | 0.28 ± 0.13
473 | 4.41 ± 12.2 | 0.27 ± 0.17 | 0.3 ± 0.32
T | q_sat | k | t | CI for q_sat | CI for k | CI for t
303 | 4.31 | 17.81 | 0.45 | [4.25 4.47] | [16.21 20.28] | [0.43 0.47]
338 | 5.58 | 9.99 | 0.34 | [5.21 5.29] | [7.82 9.2 ] | [0.36 0.36]
373 | 5.68 | 2.1 | 0.33 | [5.65 5.68] | [1.98 2.21] | [0.32 0.33]
423 | 5.77 | 0.74 | 0.31 | [5.38 5.85] | [0.73 0.78] | [0.3 0.31]
473 | 2.92 | 0.3 | 0.35 | [2.82 2.99] | [0.26 0.32] | [0.34 0.37]
    By NMA:

## Slide 14: Problem 2: MnO2-Catalyzed Acetic Acid Oxidation
Determine the parameters () in equation (3) of [2]
Object equation
    is the conversion of acetic acid
    is the catalyst mass/acetic acid molar flow rate into the reactor
Determine the 95 % confidence interval of the parameters

## Slide 15: Problem 2: MnO2-Catalyzed Acetic Acid Oxidation

## Slide 16: Problem 2: MnO2-Catalyzed Acetic Acid Oxidation
Result
    By GN-M:
    k1, k2 ,k3 = [1.16 0.88 0.61]
    CI_k1 = [ 0.72 1.59]
    CI_k2 = [-5.63 7.39]
    CI_k3 = [-0.88 2.1 ]
    By NMA:
  Validation:

## Slide 17: Click to edit Master title style