## Slide 1: CHBE 552 Project Comparison of the Simplex Optimization Method with the Gauss-Newton Method for Parameter Estimation in Algebraic Models
Jincong Li
April 7th

## Slide 2: Outline
Gauss-Newton Method with Marquardt’s Modification
Nelder-Mead Algorithm
Problem 1: Adsorption of 1,2 Dichloropropane
Problem 2: MnO2-Catalyzed Acetic Acid Oxidation

## Slide 3: Gauss-Newton Method with Marquardt’s Modification
Gauss-Newton Method for Non-Linear Least Squares:
    Aim: Minimize sum of squared differences between observed data and model predictions.
    Application: Parameter estimation in models linearizable with respect to parameters.
    Iterative Approach: Refines parameter estimates to reduce discrepancy between observed and predicted values.
    Update Formula: where J is the Jacobian matrix and r is the residuals vector.

## Slide 4: Gauss-Newton Method with Marquardt’s Modification
Marquardt’s Modification (Levenberg-Marquardt Algorithm):
    Enhancement of Gauss-Newton method, introducing a damping factor λ for robustness.
    Improves convergence, especially when the Jacobian is near singular or not invertible.
    Combined Approach: Acts like gradient descent with high λ and like Gauss-Newton with low λ.
    Modified Update Formula: adding flexibility to step size and direction.
    Goal: Achieve balance between speed (Gauss-Newton) and stability (gradient descent) in parameter estimation.

## Slide 5: Gauss-Newton Method with Marquardt’s Modification
Computing Confidence Intervals for Parameter Estimates:
    Covariance Matrix Calculation:
      Derived from the inverse of the Hessian matrix, approximated by J^T*J, where J is the Jacobian matrix.
      Use the pseudo-inverse in cases of singularity for stability.
    Standard Errors of Estimates:
      Calculated as the square root of the diagonal elements of the covariance matrix.
    Confidence Interval Calculation:
      Confidence intervals are determined using the standard errors, a critical value from the t-distribution, and the degrees of freedom.
      Formula: Estimate±(t-critical×Standard Error)

## Slide 6: Nelder-Mead Algorithm
Direct search method for minimizing an objective function.
Suitable for non-linear, non-smooth functions without requiring derivatives.
Operates using a simplex (a polytope in higher dimensions) to represent candidate solutions.

## Slide 7: Nelder-Mead Algorithm
Key Steps of the Nelder-Mead Method:
    Initialization: Generate an initial simplex around a starting point.
    Evaluation: Calculate the objective function at each simplex vertex.
    Transformation: Perform operations to update the simplex:
    Reflection: Reflect the worst point across the centroid if it improves.
    Expansion: Take a larger step if reflection finds a new best point.
    Contraction: Move the worst point closer to the centroid if reflection fails.
    Shrinkage: Reduce the simplex size around the best point for finer exploration.
    Termination: Repeat until reaching a stop condition (e.g., minimal objective function change, small simplex, maximum iterations).

## Slide 8: Nelder-Mead Algorithm
Advantages: Simple implementation, no need for derivative information, versatile across complex functions.
Limitations: Potential for slow convergence or convergence to non-optimal points, especially in rugged landscapes or high dimensions.
Applications: Ideal for parameter estimation in models where gradient-based methods are inapplicable due to lack of derivatives or presence of many local minima.

## Slide 9: Nelder-Mead Algorithm
Advantages: Simple implementation, no need for derivative information, versatile across complex functions.
Limitations: Potential for slow convergence or convergence to non-optimal points, especially in rugged landscapes or high dimensions.
Applications: Ideal for parameter estimation in models where gradient-based methods are inapplicable due to lack of derivatives or presence of many local minima.

## Slide 10: Nelder-Mead Algorithm
Bootstrap Method Overview:
    A statistical tool to estimate the distribution of a statistic (e.g., mean, variance) from data.
    Involves sampling with replacement to create many "bootstrap samples."
    Computes the statistic for each bootstrap sample to generate a distribution.
Key Steps:
    Resampling: Randomly sample with replacement from the original data to create bootstrap samples.
    Computation: Calculate the statistic of interest for each bootstrap sample.
    Repetition: Repeat the resampling and computation steps many times to build a distribution.
    Estimation: Use the distribution to estimate confidence intervals or variance of the statistic.

## Slide 11: Problem 1: Adsorption of 1,2 Dichloropropane
Determine the parameters () of the adsorption model (equation 1) of [1]
    : amount adsorbed
    : saturation amount adsorbed
    : equilibrium constant
    : pressure
    : parameter that characterizes the system heterogeneity
Determine the 95 % confidence interval of the parameters

## Slide 12: Problem 1: Adsorption of 1,2 Dichloropropane
Figure 1: Raw Data for Problem [1]

## Slide 13: Problem 1: Adsorption of 1,2 Dichloropropane
Result
    By GN-M:
Validation
T | q_sat | k | t
303 | 4.31 ± 0.19 | 17.73 ± 5.73 | 0.46 ± 0.05
338 | 5.2 ± 0.56 | 7.99 ± 2.6 | 0.37 ± 0.05
373 | 4.56 ± 1.09 | 1.72 ± 0.41 | 0.38 ± 0.07
423 | 6.77 ± 6.75 | 0.8 ± 0.23 | 0.28 ± 0.13
473 | 4.41 ± 12.2 | 0.27 ± 0.17 | 0.3 ± 0.32
T | q_sat | k | t | CI for q_sat | Ci for k | CI for t
303 | 4.31 | 17.81 | 0.45 | [4.25 4.47] | [16.21 20.28] | [0.43 0.47]
338 | 5.58 | 9.99 | 0.34 | [5.21 5.29] | [7.82 9.2 ] | [0.36 0.36]
373 | 5.68 | 2.1 | 0.33 | [5.65 5.68] | [1.98 2.21] | [0.32 0.33]
423 | 5.77 | 0.74 | 0.31 | [5.38 5.85] | [0.73 0.78] | [0.3 0.31]
473 | 2.92 | 0.3 | 0.35 | [2.82 2.99] | [0.26 0.32] | [0.34 0.37]
    By NMA:

## Slide 14: Problem 2: MnO2-Catalyzed Acetic Acid Oxidation
Determine the parameters () in equation (3) of [2]
Object equation
    is the conversion of acetic acid
    is the catalyst mass/acetic acid molar flow rate into the reactor ratio
Determine the 95 % confidence interval of the parameters

## Slide 15: Problem 2: MnO2-Catalyzed Acetic Acid Oxidation

## Slide 16: Problem 2: MnO2-Catalyzed Acetic Acid Oxidation
Result
    By GN-M:
    k1, k2 ,k3 = [1.16 0.88 0.61]
    CI_k1 = [ 0.72 1.59]
    CI_k2 = [-5.63 7.39]
    CI_k3 = [-0.88 2.1 ]
    By NMA:
  Validation:

## Slide 17: Click to edit Master title style