## Slide 1: Verification and Validation of Numerical Modelling of DTMB 5415 in Head Wave Condition
M.Eng Project
Jincong Li
Aug 16th , 2024

## Slide 2: Outline
Introduction
    Project
    DTMB 5415
Methodology
Result
Discussion

## Slide 3: Introduction
Problem Statement:
  Verify and validate the numerical modeling of the DTMB5415 in head wave conditions using Simflow.
Comparison with Experimental Data:
  Conduct a detailed comparison between the simulation results obtained from Simflow and the available experimental data, particularly in terms of vertical shear force.
Sensitivity Analysis:
  Perform a sensitivity analysis to determine the impact of various simulation parameters, such as mesh size, on the accuracy and stability of the results.

## Slide 4: DTMB 5415
David Taylor Model Basin
Specifications
Figure 1: DTMB 5415
Sonar Dome
Transom stern

## Slide 5: Numerical Simulation
Significance
Simflow
    CFD: N-S Equations
    Output integrated force
  Advantage

## Slide 6: Computational Domain & Boundaries
Figure 2: Computational Domain

## Slide 7: Wave
Second Order Stokes Head Wave
  Wave length = L_OA of 1/24 DTMB ship model
  Wave height = 1/50 of the wavelength
  Wave period = 1.34 second

## Slide 8: Mesh
Gmsh: 2 millions of tetrahedra elements
Figure 3: Mesh of the Domain

## Slide 9: Mesh
Figure 4: 3D view of the Mesh

## Slide 10: Parameters
Water density = 1000 kg/m^3
Air density= 1.225 kg/m^3
Water viscosity = 1.002e-3 m^2/s
Air viscosity = 1.983e-5 m^2/s
Gravity = (0, 0, -9.81) m/s^2
Dt = 0.05s

## Slide 11: Data
Simflow output .oisd file
MATLAB script

## Slide 12: Result

## Slide 13: Non-dimensional Vertical Shear Force

## Slide 14: Mesh Convergence Tests
1.6 millions to 2.1 millions
<1.6 millions: unphysical result
>2.1 millions: performance limitation
Figure 5: MCT

## Slide 15: Discussion
Success of the simulation with 3.36% error of non-dimensional VSF
Effectiveness of Simflow
Improvement of accuracy when the mesh in finer close to the ship model
Significance of the mesh quality and configuration in numerical method
Significance of this study and implications

## Slide 16: Limitation & Future Work
Head wave, beam wave and other wave conditions
Computational cost
Heave, pitch and yaw motion - FSI
Intact vs damaged ship

## Slide 17: Click to edit Master title style